## Slide 1
Computer Organization and Architecture
ETCS-204
Dr. Deepak Gupta
Computer Science & Engineering
Maharaja Agrasen Institute of Technology, Delhi (GSIPU)
Email: drdeepakgupta.cse@gmail.com, deepakgupta@mait.ac.in
Web: sites.google.com/view/drdeepakgupta

## Slide 7: Instruction code format
Instruction code format with two parts : Op. Code + Address
  Op. Code : specify 16 possible operations(4 bits)
  Address : specify the address of an operand(12 bits)
  If an operation in an instruction code does not need an operand from memory, the rest of the bits in the instruction(address field) can be used for other purpose
Op. Code Address
15 12 11 0
instruction
data
15 12 11 0
Not an instruction

## Slide 8: Components of Instructions
Operations (opcodes)
Number of operands (Number of data locations)
opcode:add value in src1 to
value in src2 and place the
result in dst.
ADD R1, R2, R3 R1  R2 + R3
Instruction encodings
add r1,r2,r3
src2
dst
opcode
src1

## Slide 9: Number of Operands per instruction
No Operands HALT NOP
1 operand NOT R4 R4  R4
2 operands ADD R1, R2 R1  R1 + R2
3 operands ADD R1, R2, R3 R1  R2 + R3
> 3 operands MADD R4,R1,R2,R3 R4  R1+(R2*R3)
Each specify one operation and 1,2, 3 or 4 data locations.
Notes: 9

## Slide 10: Instructions are read from memory as words
Instructions can be formatted to fit in one or more memory words.
An instruction may contain
  An opcode + data (immediate operand)
  An opcode + the address of data (direct addressing)
  An opcode + an address where the address of the data is found (indirect addressing)
  Data only (location has no instructions)
  An opcode only (register-reference or input/output instruction)
Notes: 10